## Slide 1: Motivation for looking at AERONET inversion products
The simple linear association between satellite AOD and PM is not generally that strong (R2~0.01-0.3)
Rely on meteorology, land use, chemical transport models, spatial and temporal variables in complex, adjusted models
  AOD not necessarily the “best” or most important variable in predicting PM mass or PM speciation
Key Questions:
  Can we calibrate AOD-PM at AERONET sites and reliably apply these models to satellite AOD?
  What properties can we retrieve that associate best with PM and PM speciation?

## Slide 2: Takeaways from AERONET sunphotometer
Co-located AERONET and PM2.5 sites from the DRAGON campaign in California Central Valley
Linear regression (R2=0.35) is significantly improved with spatial and temporal terms.
The longer time series at Fresno has the largest contribution to improved R2 and RMSE.
The AERONET-calibrated models perform comparably when applied to convert satellite (MISR) AOD.
Sorek-Hamer, M., Franklin, M., Chau, K., Garay, M., & Kalashnikova, O. (2020). Spatiotemporal Characteristics of the Association between AOD and PM over the California Central Valley. Remote Sensing, 12(4), 685.

## Slide 3: Takeaways from MISR
Sulfate
Nitrate
EC
Dust
PM2.5
Using MISR AOD types and mixtures we find that total AOD is not necessarily the most important variable:
For mass, sulfate, nitrate AOD types (small, medium, non-spherical)
For EC, AOD is 8th most important
For dust, the mixtures (combination of MISR types) are most important
Chau, K., Franklin, M., & Gauderman, W. J. (2020). Satellite-Derived PM2.5 Composition and Its Differential Effect on Children’s Lung Function. Remote Sensing, 12(1028).

## Slide 4: AERONET Inversion Products
AERONET sites have a retrieved “inversion” product providing optical components (40+).
The retrieval uses Optimal Estimation (Dubovik et al), MAIA is implementing similar retrieval.
These sites are also co-located EPA AQS and chemical speciation monitors (CSN) where we have ions, metals, carbons

## Slide 5: Co-located AERONET - PM Summary
We see expected regional trends
  Mass concentrations higher in west
  Nitrate concentrations higher in west
  Sulfate concentrations higher in east
  EC concentrations higher in east
  OC concentrations higher in west
Region | N mass | PM2.5 mean(sd) | N spec | PM2.5 Sulfate mean(sd) | PM2.5 Nitrate mean(sd) | PM2.5 EC mean(sd) | PM2.5 OC mean(sd)
West | 3248 | 14.1 (12.6) | 554 | 1.1 (0.46) | 3.4 (5.5) | 0.74 (0.69) | 3.5 (3.4)
Central | 610 | 7.1 (3.4) | 40 | 0.51 (0.23) | 0.44 (0.55) | 0.63 (0.29) | 1.7 (0.68)
East | 715 | 8.5 (4.3) | 357 | 3.6 (3.4) | 1.7 (3.5) | 1.35 (0.81) | 2.3 (1.30)
All | 7028 | 12.2 (10.3) | 2050 | 1.9 (2.3) | 1.7 (3.5) | 0.59 (0.55) | 2.4 (2.6)

## Slide 6
Correlation Regression Tree of AERONET Products
  AOD ( 340nm-1020nm), Column Water Vapor, Angstrom Exponent, Asymmetry factor coarse/fine (440nm-1020nm), AOD Extinction coarse/fine (440nm-1020nm), Effective Radius
Correlations in meaningful clusters.
For example:
Effective radii and asymmetry factors show high positive correlations within size grouping (total, coarse, fine)
AOD at different wavelengths are also highly positively correlated with each other
Angstrom exponents (AE) at all wavelengths have correlations >0.9 (as such we selected to use only the 440-675 nm AE in linear model selection)
We used all possible subsets regression and model selection as well as XGBoost (gradient boosting)

## Slide 7: AERONET Sunphotometer – PM2.5 Results
Coincident 440nm
Mean correlation R= 0.34
Coincident 675nm
Mean correlation R= 0.33
Coincident 870nm
Mean correlation R= 0.30
Coincident 1020nm
Mean correlation R=0.27

## Slide 8: AERONET Inversion products – PM2.5 Results
The simple linear regression between AOD 550 and PM2.5 has an overall R2 = 0.27
The best linear model with the inversion products R2 =0.70 and RMSE = 5.03 ug/m3
The overall XGBoost model R2=0.76, RMSE = 5.07 ug/m3
There are regional differences
There is consistency in the inversion products selected for PM2.5 The most important variables include:
Effective Radius (Fine), Angstrom Exponent 440-675, and AOD Extinction (fine, multiple wavelengths).
Region | N mass | R2 | RMSE ug/m3 | MAE ug/m3
West | 3322 | 0.89 | 4.43 | 3.07
Central | 610 | 0.74 | 1.70 | 1.39
East | 442 | 0.81 | 2.23 | 1.65
All | 7028 | 0.76 | 5.11 | 3.49
Variable | R2
AOD Extinction 440 | 0.11
AOD Extinction 675 | 0.12
AOD Extinction 870 | 0.12
AOD Extinction 1020 | 0.11
Reff-F | 0.04
Extinction Angstrom Exponent 440-870 | 0.07
VMR-F | 0.04
VolC-F | 0.08
Inversion results XGB
Overall univariate results

## Slide 9
central
west
east
all
Overall important variables
AOD extinction fine and total at multiple wavelengths
Extinction Angstrom Exponent
St Louis

## Slide 10: Ranked top 10 across regions
var | west | rankw | east | ranke | central | rankc | ranksum
AODExtinctionFine870nm | 2.0016271 | 2 | 1.06411397 | 1 | 0.8592917 | 1 | 4
AODExtinctionFine1020nm | 1.19469448 | 3 | 0.4037702 | 4 | 0.41950583 | 3 | 10
`ExtinctionAngstrom_Exponent_440870nm-Total` | 0.96470731 | 5 | 0.11092582 | 16 | 0.50099784 | 2 | 23
AsymmetryFactorCoarse440nm | 1.00599478 | 4 | 0.1321965 | 13 | 0.21091108 | 7 | 24
StdC | 0.5918797 | 6 | 0.11716526 | 15 | 0.13503298 | 12 | 33
AODExtinctionTotal440nm | 0.20308357 | 23 | 0.23216337 | 9 | 0.23022072 | 5 | 37
AsymmetryFactorTotal1020nm | 0.43338842 | 7 | 0.22150954 | 10 | 0.07600438 | 20 | 37
AsymmetryFactorCoarse675nm | 0.32597454 | 10 | 0.10471226 | 17 | 0.15356098 | 11 | 38
VMRT | 0.393952 | 8 | 0.09362967 | 20 | 0.11537784 | 14 | 42
AODExtinctionFine440nm | 0.29737065 | 13 | 0.5310537 | 3 | 0.03392925 | 29 | 45
Region | R2
West | 0.60
Central | 0.32
East | 0.53
All | 0.43
Linear model with top 10 ranked

## Slide 11: AERONET Inversion products – PM2.5 Nitrate Results
The simple linear regression between AOD 550 and PM2.5 has an overall R2 = 0.33
The best linear model with the inversion products R2 =0.71
The overall XGBoost model R2=0.67, RMSE = 1.51 ug/m3
There are large regional differences
There is consistency in the inversion products selected for nitrate The most important variables include:
Effective Radius (Fine), Asymmetry Factors, AOD 440 nm, Angstrom exponent, Volume Median Radius.
Region | N mass | R2 | RMSE ug/m3 | MAE ug/m3
West | 3248 | 0.94 | 1.43 | 0.79
Central | 610 | 0.31 | 0.53 | 0.41
East | 715 | 0.40 | 0.94 | 0.59
All | 7028 | 0.67 | 1.51 | 1.02

## Slide 12: AERONET Inversion products – PM2.5 Sulfate Results
The simple linear regression between AOD 550 and PM2.5 has an overall R2 = 0.27
The best linear model with the inversion products R2 =0.48
The overall XGBoost model R2=0.62, RMSE = 1.43 ug/m3
There are large regional differences
There is consistency in the inversion products selected for nitrate The most important variables include:
Volume Concentration (Fine), Asymmetry Factors, Volume Median Radius, AOD 440 nm.
Region | N mass | R2 | RMSE ug/m3 | MAE ug/m3
West | 3248 | 0.81 | 0.22 | 0.16
Central | 610 | 0.35 | 0.69 | 0.48
East | 715 | 0.63 | 2.07 | 1.31
All | 7028 | 0.62 | 1.43 | 0.81

## Slide 13: AERONET Inversion products – PM2.5 EC Results
The simple linear regression between AOD 550 and PM2.5 has an overall R2 = 0.03
The best linear model with the inversion products R2 =0.32
The overall XGBoost model R2=0.41, RMSE = 0.42 ug/m3
There are regional differences (Table)
There is consistency in the inversion products selected for EC The most important variables include:
Volume Median Radius total and fine, and their standard deviations, asymmetry factor coarse and total, AOD 1020 nm.
Region | N mass | R2 | RMSE ug/m3 | MAE ug/m3
West | 3248 | 0.79 | 0.32 | 0.22
Central | 610 | 0.49 | 0.28 | 0.23
East | 715 | 0.31 | 0.77 | 0.57
All | 7028 | 0.41 | 0.42 | 0.29

## Slide 14: AERONET Inversion products – PM2.5 OC Results
The simple linear regression between AOD 550 and PM2.5 has an overall R2 = 0.09
The best linear model with the inversion products R2 =0.35
The overall XGBoost model R2=0.38, RMSE = 0.44 ug/m3
There are regional differences (Table)
There is consistency in the inversion products selected for OC The most important variables include:
Asymmetry factors (total), AOD extinction fine and coarse, Angstrom Exponent, AOD 440 nm.
Region | N mass | R2 | RMSE ug/m3 | MAE ug/m3
West | 3248 | 0.79 | 1.37 | 0.94
Central | 610 | 0.54 | 0.67 | 0.51
East | 715 | 0.51 | 1.00 | 0.82
All | 7028 | 0.63 | 1.47 | 1.00

## Slide 15: AERONET Inversion products – PM2.5 Dust Results
The simple linear regression between AOD 550 and PM2.5 has an overall R2 = 0.003
The best linear model with the inversion products R2 =0.56
The overall XGBoost model R2=0.86, RMSE = 0.55 ug/m3
There are regional differences
There is consistency in the inversion products selected for OC The most important variables include:
Volume concentrations coarse and total, asymmetry factors coarse, effective radius coarse.
Dust = 2.2Al+2.49Si+1.63Ca+1.94Ti+2.42Fe
Region | N mass | R2 | RMSE ug/m3 | MAE ug/m3
West | 3248 | 0.85 | 0.54 | 0.26
Central | 610 | 0.60 | 0.59 | 0.49
East | 715 | 0.89 | 0.16 | 0.11
All | 7028 | 0.86 | 0.55 | 0.31

## Slide 16: Summary and Conclusions
When predicting PM and PM speciation, AOD alone is not sufficient
Evidence that other optical properties can significantly improve the associations
  Specific properties relate to PM mass or PM speciation
  All subsets linear regression and XGboost yield similar variables selected for best model
  Machine learning improves R2 significantly
  Region and available time series matter: longer time series produces more data and stable models.
More targeted variable selection and machine learning methods will help inform best products for predicting PM and PM species from retrieval.